ANILAM

Procedure to replace a 486 bios battery , when installing a new battery you must auto type the Hard Drive, you must also use an external keyboard.

Battery type is a Rayovac BR2335 , 3v lithium

First , replace the battery with the power off

Turn on the machine with the external keyboard plugged in

As the computer boots , hold F2 to enter setup

Now set the time and date

Pull down to the IDE ADPTOR MASTER

It should say AUTO TYPE , press enter

The computer will automatically configure your HD

Now make sure you set all of these following items

Multi – sector         DISABLE

LBA mode              DISABLE

32-Bit I/O	         DISABLE

Transfer mode       STANDARD

PRESS ESC

Now set the NUMLOCK    OFF

Now set the C-MOS restore condition to   NEVER

And finally save settings & exit

This bios has three different pages , you access them by using the left and right arrows , some fields are set by using the +/- key , press it to toggle the option you want to change .

All the commands are displayed across the bottom of the screen.